## Slide 1: VLAN的通信

## Slide 2: VLAN间的通信需求

## Slide 3: 路由器实现VLAN间通信
路由器端口的数量问题？

## Slide 4: 单臂路由
利用802.1Q和子接口实现
存在的问题？

## Slide 5: 三层交换机的产生
二层交换和三层路由的集成

## Slide 6: 利用三层交换机实现VLAN间通信
三层路由转发引擎

## Slide 7: 交换机匹配转发模型
CPU维护路由表
ASIC芯片完成主要的数据转发
一次路由，多次交换

## Slide 8: 交换机转发表

## Slide 9: 交换机最长匹配转发表

## Slide 10: 直连VLAN间流量转发

## Slide 11: 跨设备VLAN间流量转发

## Slide 12: 单臂路由案例
S1
vlan batch 10 20 30
interface GigabitEthernet0/0/1
port link-type trunk
port trunk allow-pass vlan 2 to 4094
#
interface GigabitEthernet0/0/2
port link-type trunk
port trunk allow-pass vlan 2 to 4094
#
interface GigabitEthernet0/0/3
port link-type trunk
port trunk allow-pass vlan 2 to 4094

## Slide 13: 单臂路由案例
S2
vlan batch 10 20
#
interface Ethernet0/0/1
port link-type access
port default vlan 10
#
interface Ethernet0/0/2
port link-type access
port default vlan 20
interface GigabitEthernet0/0/2
port link-type trunk
port trunk allow-pass vlan 2 to 4094

## Slide 14: 单臂路由案例
S3
vlan batch 30
#
interface Ethernet0/0/1
port link-type access
port default vlan 30
#
interface GigabitEthernet0/0/2
port link-type trunk
port trunk allow-pass vlan 2 to 4094

## Slide 15: 单臂路由案例
R
interface GigabitEthernet0/0/1.1
dot1q termination vid 10
ip address 10.1.1.254 255.255.255.0
arp broadcast enable
#
interface GigabitEthernet0/0/1.2
dot1q termination vid 20
ip address 20.1.1.254 255.255.255.0
arp broadcast enable
#
interface GigabitEthernet0/0/1.3
dot1q termination vid 30
ip address 30.1.1.254 255.255.255.0
arp broadcast enable

## Slide 16: 三层交换机案例
S2
vlan batch 10 20
#
interface Ethernet0/0/1
port link-type access
port default vlan 10
#
interface Ethernet0/0/2
port link-type access
port default vlan 20
interface GigabitEthernet0/0/2
port link-type trunk
port trunk allow-pass vlan 2 to 4094

## Slide 17: 三层交换机案例
S3
vlan batch 30
#
interface Ethernet0/0/1
port link-type access
port default vlan 30
#
interface GigabitEthernet0/0/2
port link-type trunk
port trunk allow-pass vlan 2 to 4094

## Slide 18: 三层交换机案例
S1
vlan batch 10 20 30
interface Vlanif10
ip address 192.168.1.254 255.255.255.0
interface Vlanif20
ip address 192.168.2.254 255.255.255.0
interface Vlanif30
ip address 192.168.3.254 255.255.255.0
interface GigabitEthernet0/0/2
port link-type trunk
port trunk allow-pass vlan 2 to 4094
interface GigabitEthernet0/0/3
port link-type trunk
port trunk allow-pass vlan 2 to 4094